## Slide 1: Impact of Power Grid Structure on Energy Storage Performance
Nathan Oliver

## Slide 2: Project Targets
            Develop new methods to optimize ES performance
              ES net ability
              Betweenness
            Find the best location to install energy storage (ES) in the grid
            Determine which grids have superior structures for ES performance
            Determine grid structure factors that influence ES performance
              Capacity
              Impedance
              Density
              Number of Lines
            Provide suggestions to improve future grids for ES performance

## Slide 3: Why Energy Storage?
  About 20% of the world’s electricity will come from solar and wind in 2040.
  The issue is that generation must meet load at every instant.
    Wind and solar generation is not constant and difficult to control.
    If more than 20% of electricity comes from wind and solar, grid will encounter problems.
  How to deal with this problem?
    Energy storage (ES)
  ES essentially decouples generation from load.
Figure 1: Time shift of electricity
Power (kW)
Time of Day
PV Gen Profile
Load Profile
Time Shift

## Slide 4: Energy Storage Considerations
Size Type Location
1 Ah
5 Ah
10 Ah
Li-ion
pumped-storage
flywheel storage
Figure 2: Comparison of size, type and location for ES considerations

## Slide 5: Energy Storage Optimization
Voltage
Support
Selecting the best ES location in the grid will optimize ES performance
Frequency
Regulation
Arbitrage
ES
Performance

## Slide 6: Determine Optimal ES Siting
Figure 3: Example network
  Find the best location for ES to optimize ES performance
  Centrality
    Determine the most important or central nodes in a network
    Several different methods to analyze centrality
    Used to analyze networks in different fields of study
      Biology
      Transportation
      Logistics
  Model electrical grid as a simple network
    The grid can be defined as nodes connected by lines
4
3
2
1

## Slide 7: Pure Topological Approach
  Assumptions
    Lines are unweighted
    One path between generator and load
  This is clearly a problem
    Since not all transmission lines are equal, in terms of distance or in electrical properties.
    Electricity can take a multitude of paths between generator and load
  In order to overcome this, the physics of power flow is considered.
    A weighted model is proposed to model the physics of power flow to determine the most appropriate ES site
Figure 4: Example grid
Z1
Z2
Z3
Z4
Z5
Gen
Load

## Slide 8: Electrical Grid Considerations
  Need to consider the physics of electrical grids
  Need to determine path, distance, and rate of flow
  Bus Type
    Generator, load, or transmission bus (path)
  Transmission Lines
    Impedance (distance)
  Electrical path
    Power Transfer Distribution Factor (path and rate of flow)
  Capacity
    Grid cannot exceed power limit (rate of flow)
Gen
Load
Trans
Trans
Z1
Z2
Z3
Z4
Z5
line reaches capacity limit
Figure 5: Example grid

## Slide 9: Optimal ES Siting Methods
ES Net Ability Betweenness

## Slide 10: Net Ability
  Net ability will be used to create ES net ability
  Net ability is a well accepted measure of grid performance and has been referenced numerous times
  Net ability quantifies a grid’s structure in terms of performance
  Calculates the performance from every generator-load pair
  ES is not considered in net ability
  Installing ES will decrease installed capacity and shift energy to periods of high demand
g1
g2
d1
d2
Figure 5: Example grid with two generators and two loads

## Slide 11: Net Ability
g1
d1
g1
d1
g2
d2
g1
d2
g2
d1
g2
d2
  ( )

## Slide 12: ES Net Ability
Figure 6: Grid with ES and electricity flows only through ES
  ES is added to the grid, need to consider capacity and equivalent impedance for generator-ES pairs and ES-load pairs
  Instead of calculating the grid performance, it calculates the performance of ES at each node, i.e., ES performance
  Flow between generators and loads is not taken into account because ES net ability is only concerned with the added benefit of ES, not with the direct transmission of electricity from generator to load
g
d
e

## Slide 13: ES Net Ability
Figure 9: Flow between gen and load is disregarded,
only concerned with added benefit of ES
g
d
g
d
e
g
d
e
e
g
d
Figure 7: Grid with no ES
Figure 8: Grid with ES and flow directly from generator to load
Figure 10: Flow between gen and load is disregarded,
only concerned with added benefit of ES

## Slide 14: ES Net Ability
  Need to calculate the capacity and equivalent impedance for every generator-ES-load combination.
  The equivalent impedance and capacity between generator and ES and between ES and load are in series.
  For equivalent impedance, they can be added together since they are in series.
e
g
d
Figure 10: Capacity and equivalent impedance can be treated as elements in series

## Slide 15: ES Net Ability
  To calculate capacity in series, must consider the capacity from g to e, and from e to d, as well as ES capacity
  The capacity from g to d
  the total time from g to d equals the charge time and discharge time of ES
e
g
d
Figure 11: Capacity and equivalent impedance can be treated as elements in series

## Slide 16: Betweenness
  The original betweenness equation determined the likelihood a bus was located along the shortest path between a generator and load.
  Is similar to Kirchhoff’s Current Law, where currents in and out of each node are summed, and divided by 2.
  Betweenness equation
  Modified betweenness equation for ES
3
2
1
4
0.6
0.4
0.2
0.2
0.8
1.0
1.0
Figure 12: Betweenness calculation

## Slide 17: Case Study
Figure 13: IEEE 30 test system
  Determine the optimum ES site in IEEE test systems
    IEEE 30
    IEEE 118
    IEEE 300
  Input data from IEEE test data files into a Matlab program
  Program ranks each bus from best to worst for ES siting
    ES net ability
    Betweenness

## Slide 18: Results Optimal ES Siting

## Slide 19: IEEE 30 – Optimal ES Siting
ES net ability (red) – Bus 6
Betweenness (blue) – Bus 6
Figure 14: IEEE 30 test system with optimal ES site

## Slide 20: IEEE 118 – Optimal ES Siting
ES net ability (red) – Bus 69
Betweenness (blue) – Bus 65
Figure 15: IEEE 118 test system with optimal ES sites

## Slide 21: IEEE 300 – Optimal ES Siting
ES net ability (red) – Bus 3
Betweenness (blue) – Bus 42
Figure 16: IEEE 118 test system with optimal ES sites

## Slide 22: Why?

## Slide 23: Case Study
  Observations
    Location
      Nodes in the center of the network tend to have higher ES net ability and betweenness
    Number of connections
      Nodes connected to more lines tend to have higher ES net ability and betweenness
  The following results will only test ES net ability
Figure 17: IEEE 30 test system with optimal ES site

## Slide 24: Location
  How to determine or quantify location?
  Determine a nodes location relative to the other nodes in the network.
  A function of the sum of the distances to all the other nodes in the network
  Each line is equal to one unit in length
  Plot ES net ability vs. location to see if there is a correlation
  Higher location value leads to higher ES performance
1
2
3
4
5
1
1
2
3

## Slide 25: Number of Connections
  Sum the number of lines connected to each node
  Plot ES net Ability vs. number of connections to see if there is a correlation
  More connections leads to higher ES performance
1
2
3
4
5

## Slide 26: Results Factors of Optimal ES Siting

## Slide 27: IEEE 30, 118, 300 - Location
Figure 18: IEEE 30 – ES net ability vs. node location
Figure 19: IEEE 118 – ES net ability vs. node location
Figure 20: IEEE 300 – ES net ability vs. node location

## Slide 28: IEEE 30, 118, 300 - Number of Connections
Figure 21: IEEE 30 – ES net ability vs. connections
Figure 22: IEEE 118 – ES net ability vs. connections
Figure 23: IEEE 300 – ES net ability vs. connections

## Slide 29: Location vs. Number of Connections
Bus System | Coefficient of Determination (R2) | 
 | Node Location | Number of Connections
IEEE 14 | 0.85 | 0.81
IEEE 30 | 0.88 | 0.77
IEEE 33 | 0.47 | 0.42
New England 39 | 0.87 | 0.71
IEEE 57 | 0.89 | 0.74
IEEE 118 | 0.82 | 0.61
IEEE 300 | 0.70 | 0.40
  For all seven test systems, location had a higher R2 than number of connections
  Node location is a much stronger factor for a nodes ES net ability than number of connections
Figure 24: IEEE 118 – ES net ability vs. node location
Figure 25: IEEE 118 – ES net ability vs. connections

## Slide 30: What Makes a Grid’s Structure Better for ES Performance?

## Slide 31: Case Study
  How to determine or quantify a grids structure?
  Take the average ES net ability of all the nodes in a network.
  This is called grid ES net ability
  Compare grid ES net ability to…
    Other grid ES net ability (which grid is better)
    Impedance
    Capacity
    Lines per Node (Number of Connections)
    Density (Location)
1
2
3
4
5

## Slide 32: Results Grid Structure

## Slide 33: Grid Structure - Capacity
  Line capacities were changed and then grid ES net ability was measured
  Results show capacity and grid ES net ability are directly related
  Higher line capacity leads to better ES performance
Figure 26: IEEE 30 – Grid ES net ability vs. line capacity

## Slide 34: Grid Structure - Impedance
  Line impedances were changed and then grid ES net ability was measured
  Results show impedance and grid ES net ability are inversely related
  Lower line impedance leads to better ES performance
Figure 27: IEEE 30 – Grid ES net ability vs. line impedance

## Slide 35: Grid Structure - Lines per Node
  Grid ES net ability of seven different grids was plotted against its lines per node
  Results show that possibly having more lines with fewer nodes in a grid will lead to higher ES performance
  More data needs to be collected to verify this claim
Figure 27: IEEE 30 – Grid ES net ability vs. lines per node

## Slide 36: Grid Structure - Density
  Density of a grid is a function of the distance to other nodes in the network
  Results showed no correlation between average location (density) and grid ES net ability
  Further research will need to be performed to verify whether density leads to higher ES performance
Figure 28: Grid with low density
Figure 29: Grid with high density

## Slide 37: Conclusion
  Novel method to determine optimal ES siting
  Location of a node is a strong determinant of its ES performance. More centrally located nodes will have better ES performance.
  Can determine which grids have superior structure for ES performance
  Several factors determine a grids overall ES performance
    Impedance
      Lower impedance leads to higher ES performance
    Capacity
      Higher capacity leads to higher ES performance
    Lines per Node
      More lines may lead to higher ES performance
    Density
      Relationship unclear. More research is needed.

## Slide 38: Thank You Any Questions?